## Slide 1: EM358x Family Introduction
David Egan / Thomas Barber
FAE Summer School, April 2013

## Slide 2: Learning Objectives
In this session we are focused on the EM358x family of ZigBee SoCs
EM358x is an extension of the existing EM35x family.
Following this session you will be able to
  Identify the right Silicon Labs ZigBee product for your customer’s design
  Demonstrate the selling proposition for EM358x products
  Position the EM358x versus competition
How?
  By presenting the features of EM358x variants and what applications they enable
  By discussing how Silicon Labs Ember ZigBee tools and software work to provide a market leading ZigBee solution
  By dealing with the main competition head-on

## Slide 3: EM35x Series ZigBee System-on-Chip
  EM351 - supports ZigBee Home Automation and Network Coprocessor applications using EmberZNet PRO network protocol stack
  EM357 - full support for all ZigBee PRO application profiles including Smart Energy 1.x
  EM358x - full support for all ZigBee PRO and ZigBee IP applications including Smart Energy 2.0
Third generation ZigBee mesh networking semiconductor systems
Integrate and ARM Cortex-M3 processor and IEEE 802.15.4 RF transceiver
Industry leading performance, code density and power consumption
New
Notes: This slide highlights the main features of the EM351/EM357 products including:
ARM Cortex-M3 which can be used to run both the ZigBee software and customer applications
Integrated 2.4 GHz RF transceiver supporting IEEE 802.15.4
  ZigBee is based on the 2003 release of IEEE 802.15.4
  We do not currently support non-ZigBee protocols based on IEEE 802.15.4 on the EM351/357/358x (only ZigBee is supported today)
  We do support ZigBee IP / SE 2.0 and we are a golden unit for ZigBee IP

## Slide 4: Introducing EM358x
Market Strategy:
  EM358x is an extension of the market leading EM35x family of ZigBee SoCs
  Reduced BOM: Remove the need for external flash part (for bootloading)
  Collapse design: Reduce the number of micros required in product designs
  Complex applications: Provide more flash / ram for expanding applications
Product Roadmap/Portfolio:
  EM358x expands the EM35x family to 7 parts total to cover a range of designs
  Next generation products will be even more flexible
EM35x Variant | Flash | RAM | USB
EM3581 | 256kB | 32kB | No
EM3582 | 256kB | 32kB | Yes
EM3585 | 512kB | 32kB | No
EM3586 | 512kB | 32kB | Yes
EM3588 | 512kB | 64kB | Yes

## Slide 5: EM358x Features
Newest addition to the market-leading EM35x ZigBee SoC family
IEEE 802.15.4 transceiver
  2.4GHz frequency band
  Up to +8dBm output power
  -102dBm sensitivity @ 250kbps
  Lower MAC accelerator
  AES128 encryption accelerator
32-bit ARM® Cortex-M3
  512/256kB flash
  64/32kB RAM
High performance peripherals
  14-bit ΣΔ ADC
  Timers: Sleep, Watchdog, 4x General purpose
  Serial ports: UART, SPI, I2C, USB

## Slide 6: EM358x Enables
What can I do with extra Flash?
  Remove the external flash part used for a bootloader image, store it on EM358x
  Remove the application micro, put all of the application on EM358x
  Build flash-hungry applications like Smart Energy 2.0, with room for expansion
  Store more application data
What can I do with extra RAM?
  Run larger memory-hungry applications like Smart Energy 2.0
  Connect with more devices on larger networks
  Support an RTOS running on EM358x
What can I do with USB?
  Provide a simple application interface to an application micro
  Provide a service port to a device
  Simplify production programming

## Slide 7: Which part does my customer need?
Flash / RAM (kB) | EM351 128 / 12 | EM357 192 / 12 | EM3581/2 256 / 32 | EM3585/6 512 / 32 | EM3588 512 / 64
Small proprietary ZigBee PRO application | ✔ | ✔ | ✔ | ✔ | ✔
ZigBee Home Automation 1.x end device | ✔ | ✔ | ✔ | ✔ | ✔
ZigBee Home Automation 1.x router | ✔ | ✔ | ✔ | ✔ | ✔
Network Coprocessor device (non-Smart Energy) | ✔ | ✔ | ✔ | ✔ | ✔
ZigBee Light Link 1.0 end device |  | ✔ | ✔ | ✔ | ✔
ZigBee Light Link router |  | ✔ | ✔ | ✔ | ✔
ZigBee Smart Energy 1.x NCP device |  | ✔ | ✔ | ✔ | ✔
ZigBee Smart Energy 1.x end device |  | ✔ | ✔ | ✔ | ✔
ZigBee Smart Energy 1.x router |  | ✔ | ✔ | ✔ | ✔
ZigBee Smart Energy 2.0 IP modem device |  | ✔ | ✔ | ✔ | ✔
ZigBee Smart Energy 2.0 end device or router |  |  | ✔ | ✔ | ✔
Integrated OTA image storage (ZHA) |  |  | ✔ | ✔ | ✔
Integrated OTA image storage (ZLL / ZSE) |  |  |  | ✔ | ✔
Full gateway device with USB |  |  |  |  | ✔

## Slide 8: ZigBee Competition
 | Silicon Labs EM35x | TI CC2538 | Atmel Atmega RFR2 | NXP JN516x
Core type | Cortex-M3 | Cortex-M3 | RISC | RISC
Flash | 128-512kB | 128-512kB | 64-256kB | 64-256kB
RAM | 12-64kB | Up to 32kB | 8-32kB | 8-32kB
TX power | +8dBm max | +7dBm max | +3.5dBm | +2.5dBm max
RX sensitivity | -102dBm max | -97dBm max | -100dBm | -95dBm max
Link budget | 110dB max | 104dB max | 103.5dB max | 97.5dB max
RX current | 27mA (w/CPU) | 23mA (CPU idle) | 10.1mA (w/ CPU) | 17mA (no CPU)
TX current | 32mA (w/CPU) | 24mA (CPU idle) | 18.6mA (w/CPU) | 15mA (no MCU)
Sleep current (w/ RAM retained) | 0.8/1.25uA (w/ timer) / 0.4/1.0uA (no timer) | 1.3uA (w/ timer) / 0.4uA (no timer) | 1.5uA (w/ timer) / 0.75uA (no timer) | 1.5uA (w/ timer) / 1.02uA (no timer)
USB | Yes | Yes | No | No
Multi-Network | 1 radio on 2 PANs | Dual profile support | Multiple PAN filter | No
Local Storage Bootloader | Yes | Yes | No | No
Enhanced Security | Secure Bootloader | RSA HW acceleration |  | 
Other | Packet Trace |  | EEPROM Antenna diversity Adjust data rate | EEPROM Antenna diversity Time of flight

## Slide 9: EM35x Key Product Strengths
Hardware
  World Class RF performance  longer range/more reliable networks
  Industry leading CPU performance  enables single-chip systems
  Ultra-low standby current  up to 10 years of battery life
Software
  Best-in-class ZigBee stack and application layer  reliable/scalable network
  ZigBee Alliance certifiable reference application code  faster time to market
Tools
  Unique packet trace capability enables full network analysis  fast debug
  Simple graphical Ember AppBuilder interface  ZigBee certifiable applications
Technology leadership
  Chair several ZigBee Alliance committees  driving next generation features
  Leading the development of ZigBee IP  only open standard for 6LoWPAN
Notes: The slides should be used to reinforce the idea that the value of the Silicon Labs ZigBee solution goes beyond the hardware. The software and tools are a big part of the product differentiation.

## Slide 10: EM35x – More than a datasheet
Multi-Networks – Single EM35x connect to two ZigBee networks
    Networks can be on different PAN IDs and different frequency channels
    Example 1: Coordinator on ZHA network / End Device on ZSE network
      Allows home network to access meter data for rate and usage information
    Example 2: Coordinator on ZLL network / End Device on ZHA network
      Allows a ZLL light bulb to be controlled by either both ZLL or ZHA networks
Secure bootloader – end-to-end security for upgrades
  Bootload image is encrypted at the factory
  Image is only decrypted when it is bootloaded into the device
  Highly desired feature for Smart Energy networks
Module Partnerships
  Module partners provide ZigBee hardware and software expertise to make adding ZigBee to a design easy for our customers
  Each region / distributor should have their preferred ZigBee module partner

## Slide 11: Why do we win with EM35x?
Market Leadership
  Our customers know that we lead the ZigBee market
  Our expertise and experience comes through in our products, tools, support
  Our customers know they can build successful products
Best in class silicon
  We match and beat the competition in many areas, especially RF performance
Superior ZigBee PRO software stack
  Robust, scalable networking stacks come from years of testing, experience
  No-one has more experience certifying ZigBee software stacks and applications
Unique approach to tools
  Ember Desktop is unique – no-one else has such powerful debugging tools
  Our tools start with our chip design, leading to rich data about network activity
  Ember AppBuilder ensures that customers build interoperable products easily

## Slide 12: EM358x Development Tools
Ember Desktop provides a macroscopic view of the entire network from single console
Ember Desktop
Packet Trace Port reaches deep inside the silicon to trace packets and to monitor and control the application.
Packet Trace Port
Debug Adapter provides a high-speed back-channel link between Desktop Network Analyzer and node
Debug Adapter
Upon launch of EM358x, all new EM35x Development kits will contain EM358x
EM358x uses all the same familiar tools;
Adding EM358x to existing EM35x Development Kit is easy!
Notes: This slides highlights the benefits of the development tools that are provided with the Ember ZigBee solution. The key message is that the tools enable a unique programming and network debugging environment. The customer has full visibility into the network to enable development and debugging of complex networks. The Ethernet backchannel allows networks to be debugged remotely across a standard local area network (LAN). Results in a higher quality more reliable product and faster time to market.
Packet Trace Port—hardware based packet monitoring records each packet transmitted or received and makes it available through a simple two wire serial port
Debug Adapter—provides a bridge between the Packet Trace Port and the Desktop Network Analyzer using a standard Ethernet connection. Can be powered by PoE to reduce wiring required.
Ember Desktop —GUI that allows the user to view the activity of any node in the network and trace the activity through the applications and network layers down to the packets transferred over the network. Enables fast debugging of network activity.
Development Kits—contain all of the hardware/software required for a customer to develop a simple 2-3 node network.
- Hardware: Radio control modules (3), breakout board (3), debug adapter (3), variety pack of EM35x modules, 8-Port switch with POE, all cables necessary to connect the equipment
- Software: Desktop Network Analyzer, Ember AppBuilder, IAR Embedded Workbench (either 30-day trial or 1-year license)
EM35x NCP Add-on Kit—contains additional hardware to use the EM35x as a Network Co-Processor (NCP)
- Hardware: EM35x NCP breakout board, EM35x module, STM32 host module, battery pack
EM358x hardware includes an EM3588 module and breakout board (with USB).
This will be available as separate parts that can be added to an EM35x Development Kit
New EM35x Dev Kits after launch will include some EM3588 modules and breakout boards.

## Slide 13: EM358x Availability
Currently running Beta program with 10 key customers
  ZigBee PRO stack, tools, EM358x chips and development kit hardware
EmberZNet PRO 5.0 Software release – April 2013
  Supports EM358x platform including USB
  Introduces Local Storage Bootloader (OTA Bootloader using on-chip flash)
  Introduces Secure Bootloader feature
EM358x release schedule
  Pre-Production – May 2013
  Initial Production – June 2013  launch July 2013
  Full Production – September 2013
Collateral
  EM358x datasheet available under NDA until launch
  These slides, more to come with launch

## Slide 14: Summary
New expanded range of the most popular ZigBee SoCs
  Up to 512kB Flash  larger applications or eliminate external Flash / 2nd micro
  Up to 64kB RAM  larger applications, larger networks, IP networking
  Optional USB  application interface / service port / production bootload
Match customer requirements to the right EM35x product
  ZigBee profile: Home Automation, Smart Energy, Light Link
  System partitioning: system-on-chip or network coprocessor
  Application: Battery powered end device, router or application gateway
How to sell EM35x versus ZigBee competitors
  Unique tools  faster time to market & higher quality products
  Market leading software  reliability, robustness, scalability, interoperability
  EM35x family of parts for every ZigBee design

## Slide 15: Call to Action
Introduce EM358x to existing ecosystem
  Smart Energy customers: Meters, displays, hubs that need to connect to HAN
  Smart Energy customers who are considering Smart Energy 2.0
  Home Automation customers who want to eliminate external Flash
  Any customer looking to reduce the number of micros in their device
Identify new opportunities in key market segments
  Home automation market drivers (e.g. Comcast, TimeWarnerCable, Lowe’s)
  Smart energy ecosystem drivers (e.g. government regulators, utilities)
Contact us for assistance:
US / APAC: Thomas Barber (thomas.barber@silabs.com)
EMEA: David Egan (david.egan@silabs.com)

## Slide 16: www.silabs.com/Wireless

## Slide 17: Silicon Labs ZigBee SoCs
 | EM351 | EM357 | EM3581 | EM3582 | EM3585 | EM3586 | EM3588
Core type | Cortex-M3 | Cortex-M3 | Cortex-M3 | Cortex-M3 | Cortex-M3 | Cortex-M3 | Cortex-M3
Flash | 128kB | 192kB | 256kB | 256kB | 512kB | 512kB | 512kB
RAM | 12kB | 12kB | 32kB | 32kB | 32kB | 32kB | 64kB
USB | No | No | No | Yes | No | Yes | Yes
Sleep current | 0.8uA / 0.4uA | 0.8uA / 0.4uA | 1.25uA / 1.0uA | 1.25uA / 1.0uA | 1.25uA / 1.0uA | 1.25uA / 1.0uA | 1.25uA / 1.0uA
Max TX Power | +8dBm | +8dBm | +8dBm | +8dBm | +8dBm | +8dBm | +8dBm
Max RX Sensitivity | -102dBm | -102dBm | -102dBm | -102dBm | -102dBm | -102dBm | -102dBm
Package | QFN-48 | QFN-48 | QFN-48 | QFN-48 | QFN-48 | QFN-48 | QFN-48

## Slide 18: EmberZNet PRO Software
Complete ZigBee PRO Feature Set Stack (Most Deployed ZigBee Stack!)
  True mesh routing
  Stochastic Addressing
  Fragmentation
  Standard Security
  Frequency Agility
  PAN ID Conflict Resolution
  Many-to-one routing
  Ember ZNET PRO
  Enhanced Features
  Asymmetric links
  Intelligent table management
  Single stack for end point, router & coordinator
Flexible Utilities
  Full-featured bootloader options
  Robust Mfg test libraries
  Powerful debug options
Certifiable Reference Applications
  Certified HA, SE & LL Profile applications
  Full ZigBee Cluster Library (ZCL) implementations
  Flexible APIs
  Ember AppBuilder Tool
Customer Applications
Reference Apps
Utilities
EM351/EM357
Ember ZNet PRO Stack
Development Tools
Notes: This slide highlights the main feature of the EmberZNet PRO protocol stack software. The EmberZNet PRO stack is the most robust, scalable and mature ZigBee PRO stack available. The first seven features listed on the left side are all standard ZigBee features. The last three features are unique to the EmberZNet PRO stack from Silicon Labs.
The asymmetric link feature ensures the link is good in both directions before connected two nodes. This is critical in networks with devices from multiple vendors whose transmit output power and receive sensitivity are different.
Intelligent table management enables denser networks by forcing the routers to chose neighbors that cannot communicate directly. This enables messages to get out of dense networks (like a building utility center with hundreds of electric meters) with fewer hops which improves the bandwidth and latency of dense networks.
Unlike other ZigBee solutions, the EmberZNet PRO stack can be configured as an end point, router or coordinator at run time. The allows for more flexibility in both the device and network design.
ZigBee PRO stack (EmberZNet PRO)
These are all standard features of the ZigBee PRO stack.
True mesh routing—routes chosen my link quality. Network self-heal if a route breaks.
Stochastic addressing—enables the network to scale to thousands of nodes
Fragmentation—enables support of messages longer than the maximum payload for a given burst
Standard security—128-bit security is standard for ZigBee
Frequency agility—allows an entire network to switch frequency if there is a new source of interference
PAN ID conflict resolution—enables selection of a new PAN ID if there is a conflict with another network
Many-to-one routing—reduces network traffic by enabling a single broadcast message to multiple end-points.
Certifiable Reference Applications
Solutions for Home Automation (HA), Smart Energy (SE) and Light Link (LL) profiles available.
ZCL = Zigbee Cluster Library  basic functions that are used to build ZigBee applications profiles
  ZCL can be used to develop ZigBee standard profiles that are not currently supported by Silicon Labs or to develop custom applications profiles
Ember AppBuilder tool is a simple graphical interface that enables quickly building ZigBee compliant applications (see later slide for more details).
Flexible Utilities
Full-featured bootloader—enables local or over the air (OTA) reprogramming of the stack and applications code
Robust manufacturing test library—allows the same software image to be used for manufacturing test and normal operation
Powerful debug options—enables full visibility into network for debug and testing (see “Development Tools” slide for more details)

## Slide 19: Ember Desktop
True network-level development platform:
  Network-wide view of all packet activity
  Decodes all standard ZigBee ZCL commands/activity
  Correlates network traffic into higher-level events
  Leverages Ethernet out-of-band “backchannel” to provide true activity
  Custom decoding and filtering options
Online Video Demos:
http://www.silabs.com/products/wireless/zigbee/Pages/zigbee-training-videos.aspx
Notes: This slide highlights the features of the Ember Desktop. Ember Desktop enables fast network debugging by providing multiple views of the network activity allowing users to quickly spot time periods of interest, view the transactions both graphically and in text and look at the packets transferred during each transaction.
Filtering can be applied to each level of the activity to allow users to quickly identify nodes, transactions, packets and other parameters of interest.
The top section of the screen (mostly black) shows the overall network activity. This can be used to quickly identify time periods of interest (heavy activity, light activity, etc)
The second section (with the arrow) graphically illustrates the type of transaction being highlighted (in this case a unicast from “thing01” to “0000”)
- This section can be customized to show details about the location and or relationship between the nodes
The third section is a transaction level view of the activity for the given time period. The transaction view interprets the ZigBee cluster activity and displays the activity in more descriptive terms.
The Fourth section is a packet level view of the activity. This shows all of the packet level transfers for the given transaction.

## Slide 20: Ember AppBuilder
Generates complete, ready for certification “template application”
  Enables “ZigBee Certified Products” based on standard application profiles
Simple graphical interface to select device and network parameters
  Device type, commands and behaviors
  Automatically includes the ZigBee Cluster Library (ZCL) attributes and reporting
  Network forming and joining behaviors
  Security modes and operation
Easy vendor customizations
  Simply add vendor-specific code to complete the application
ZigBee Cluster Library
Closures
Others…
Safety & Security
Lighting
Measurement & Sensing
HVAC
General
Others…
Commercial Building Auto.
Application Profiles
AMI
Home Automation
Notes: This slide highlights the benefits of the Ember AppBuilder tool.
The Ember AppBuilder tool provides a graphical interface allowing customers to quickly configure one of the existing applications profiles (Smart Energy, Home Automation or Light Link) or build new applications profiles using the ZigBee Cluster Library (ZCL). The Ember AppBuilder enables fast/easy development of products ready for ZigBee Certified Product testing.
The Ember AppBuilder tool also provide a graphical interface for configuration of the network and each device in the network.
The output from the Ember AppBuilder tool is source code the can be compiled to run either on the EM351/57 or another host processor. Customers can easily add their own device specific code into the Ember AppBuilder output to create complete applications.